LimeRFE 1v31

Measurement Results

Version: 1.0
Revision: 6
Date: 12.03.2021

# LimeRFE 1v31 Performance Summary
Measured results of the several prototype boards are given in the table bellow.

No.	Band	TX					RX
		Gain [dB]			OP1dB [dBm]			Gain [dB]			NF [dB]			IIP3 [dBm]
		Min	Nom	Max	Min	Nom	Max	Min	Nom	Max	Min	Nom	Max	Min	Nom	Max
1	WB 1000	27		45	22.5		28.5	17		21.8	3.4		4.4	11.5		18
2	WB 4000	12		33	14		24	7.8		18.4	2.7		5.5	10		23
3	HAM 30
	5 – 30 MHz		38			33			21			6			15
	1 – 5 MHz					/		0		14
4	HAM 50-70		37			32			19			3.5			14
5	HAM 145		31			34			18			3.7			12.6
6	HAM 220		33			34			18			3.7			14.8
7	HAM 435		33			34			15			4			10
8	HAM 920		35			30			17			2.8			16
9	HAM 1280		31			31			16			2.8			20
10	HAM 2400		41			28.5			13			3.8			15.5
11	HAM 3500		33			25			7.5			4.5			12.5
12	Cell Band 1		37			28			11			6.5			19
13	Cell Band 2		40			30.5			12			5.5			19.5
14	Cell Band 3		40			29.5			13			6			19
15	Cell Band 7		37			26			8			6			21
16	Cell Band 38		38			26			8			6			20

# Setup

Measurements results were corrected by 46 dB to account for the setup.
So, approximately, the additional setup contribution is:
@ 2.0 GHz approx. 0.8 dB
@ 2.5 GHz approx. 1.2 dB
@ 3.5 GHz approx. 1.5 dB
This additional setup contribution was not de-embedded from the results.

Figure 1: Setup gain
Measurement results are from the board #2.

# TX

## Wideband 1 – 1000 MHz

Figure 2: Gain	Figure 3: Output P1dB

HF Performance
The following graphs present the performance of the Wideband 1 – 1000 MHz channel for HF frequencies.

Figure 4: Gain (HF Band)	Figure 5: Output P1dB (HF Band)

## Wideband 1000 – 4000 MHz

Figure 6: Gain	Figure 7: Output P1dB

## HAM 30 MHz (HF)

Figure 8: Gain	Figure 9: Output P1dB

## HAM 50 – 70 MHz (6 & 4 m)

Figure 10: Gain	Figure 11: Output P1dB

## HAM 144 – 146 MHz (2 m)

Figure 12: Gain	Figure 13: Output P1dB

## HAM 220 – 225 MHz (1.25 m)

Figure 14: Gain	Figure 15: Output P1dB

## HAM 430 – 440 MHz (70 cm)

Figure 16: Gain	Figure 17: Output P1dB

## HAM 902 – 928 MHz (33 cm)

Figure 18: Gain	Figure 19: Output P1dB

## HAM 1240 – 1325 MHz (23 cm)

Figure 20: Gain	Figure 21: Output P1dB

## HAM 2300 – 2450 MHz (13 cm)

Figure 22: Gain	Figure 23: Output P1dB

## HAM 3300 – 3500 MHz (9 cm)

Figure 24: Gain	Figure 25: Output P1dB

## Cellular Band 1

Figure 26: Gain	Figure 27: Output P1dB

## Cellular Band 2

Figure 28: Gain	Figure 29: Output P1dB

## Cellular Band 3

Figure 30: Gain	Figure 31: Output P1dB

## Cellular Band 7

Figure 32: Gain	Figure 33: Output P1dB

## Cellular Band 38

Figure 34: Gain	Figure 35: Output P1dB

# RX

## Wideband 1 – 1000 MHz

Figure 36: Gain	Figure 37: Noise Figure*

* Note: Extreme NF values resulted from inadequate EM isolation of the measured device. These values have not been taken into account in the Summary.
Figure 38: Input IP3

HF Performance
The following graphs present the performance of the Wideband 1 – 1000 MHz channel for HF frequencies.

Figure 39: Gain (HF Band)	Figure 40: Input IP3 (HF Band)

## Wideband 1000 – 4000 MHz

Figure 41: Gain	Figure 42: Noise Figure

Figure 43: Input IP3

## HAM 30 MHz (HF)

Figure 44: Gain	Figure 45: Noise Figure*

* Note: Extreme NF values resulted from inadequate EM isolation of the measured device. These values have not been taken into account in the Summary. NF measurements below 10 MHz are not valid, since the noise head used was not calibrated at these frequencies.
Figure 46: Input IP3**

** Note: Why does the IP3 deteriorates for frequencies below 5 MHz? This issues will be further investigated.
## HAM 50 – 70 MHz (6 & 4 m)

Figure 47: Gain	Figure 48: Noise Figure *

Figure 49: Input IP3

## HAM 144 – 146 MHz (2 m)

Figure 50: Gain	Figure 51: Noise Figure

Figure 52: Input IP3

## HAM 220 – 225 MHz (1.25 m)

Figure 53: Gain	Figure 54: Noise Figure

Figure 55: Input IP3

## HAM 430 – 440 MHz (70 cm)

Figure 56: Gain	Figure 57: Noise Figure

Figure 58: Input IP3

## HAM 902 – 928 MHz (33 cm)

Figure 59: Gain	Figure 60: Noise Figure

Figure 61: Input IP3

## HAM 1240 – 1325 MHz (23 cm)

Figure 62: Gain	Figure 63: Noise Figure *

* Note: Extreme NF values resulted from inadequate EM isolation of the measured device. These values have not been taken into account in the Summary.
Figure 64: Input IP3

## HAM 2300 – 2450 MHz (13 cm)

Figure 65: Gain	Figure 66: Noise Figure

Figure 67: Input IP3

## HAM 3300 – 3500 MHz (9 cm)

Figure 68: Gain	Figure 69: Noise Figure

Figure 70: Input IP3

## Cellular Band 1

Figure 71: Gain	Figure 72: Noise Figure*

* Note: Extreme NF values resulted from inadequate EM isolation of the measured device. These values have not been taken into account in the Summary.
Figure 73: Input IP3

## Cellular Band 2

Figure 74: Gain	Figure 75: Noise Figure *

* Note: Extreme NF values resulted from inadequate EM isolation of the measured device. These values have not been taken into account in the Summary.
Figure 76: Input IP3

## Cellular Band 3

Figure 77: Gain	Figure 78: Noise Figure

* Note: Extreme NF values resulted from inadequate EM isolation of the measured device. These values have not been taken into account in the Summary.
Figure 79: Input IP3

## Cellular Band 7

Figure 80: Gain	Figure 81: Noise Figure

* Note: Extreme NF values resulted from inadequate EM isolation of the measured device. These values have not been taken into account in the Summary.
Figure 82: Input IP3

## Cellular Band 38

Figure 83: Gain	Figure 84: Noise Figure *

* Note: Extreme NF values resulted from inadequate EM isolation of the measured device. These values have not been taken into account in the Summary.
Figure 85: Input IP3